LOCOST CAR CLUB OF WESTERN AUSTRALIA

ENGINEERING APPROVAL SUBMISSION

FOR COMPLETED LOCOST SPORTSCAR

Ref number 01- 0305

Locost Car Club of Western Australia,

www.geocities.com/darren_ponton/locostwa.htm

Meets first Thursday each month

Blue Gum Recreation Centre???

BRENTWOOD?????

Phone/fax O8 9390 7353

CONTENTS

1.	INTRODUCTION

2.	VEHICLE DESCRIPTION

3.	STATEMENT OF AUSTRALIAN DESIGN RULE (A.D.R.) COMPLIANCE

4.	CERTIFICATE OF CONFORMITY

APPENDICES:

APPENDIX A		LOCOST DIAGRAMS

APPENDIX B	ENGINEERING CHASSIS UPGRADE DRAWINGS

1.

INTRODUCTION

The Locost Sportscar is based on the design published in Ron Champion’s book ‘How to Build your Own Sports Car’ (ISBN 1 85960 636 9.), first published by Haynes Motorbooks in 1996, with an updated second edition published in 2000. The design of the Locost Sportscar chassis is similar to that of the Westfield kit car, which until recently was produced in Western Australia, and both are derived from the Lotus Super Seven of 1957. Ron Champion’s book has gone on to become Haynes publishing’s largest selling single books, and over one thousand of these cars has been completed in the United Kingdom since 1996. A worldwide club exists, with the Locost Car Club of Western Australia, being the local affiliate. The durability of the design is confirmed by the success of the ‘one-make’ Locost Racing series in the United Kingdom, administered by the ‘750 Motor Club’.

As at April 2001, there are approximately 100 cars under construction in all States and Territories of Australia, with 4 registered in South Australia, 5 in Queensland and 2 in New South Wales.

Locost Cars are not ‘kit’ cars as such, and could be described as ‘project’ cars as many of the parts are fabricated from scratch, including where appropriate, crafted by the owner/builder themselves. As such each car takes longer to complete than a conventional ‘kit’, and arguably more care and patience expressed by the builder. Cars produced by Locost Car Club of Western Australia members are built to a higher standard than specified by the book, using engineering drawings produced in consultation with Replica Cars, Unit 3/55 Poole Street, Welshpool, 6106. Club members’ vehicles are inspected by an Authorized Signatory who issues the attached Certificate of Conformity for the vehicle to assist the Department of Transport in approving the vehicles for registration.

This Engineering Approval Submission is submitted by/on behalf of:

Name (or agent):	___________________________

Address:		___________________________

Telephone:		__________________________

Fax:			__________________________

Email:			__________________________

2.	VEHICLE DESCRIPTION

The Locost Sportscar comprises:

A mild steel space frame with structural mild steel and aluminium infill panels and non-structural glass reinforced fibre bodywork. Extensive use is made of proprietary parts from common ‘donor’ vehicles that have Australian Design Rule Compliance. Suspension members are tubular mild steel (minimum) front wishbones and live rear axle mounted by radius arms and Panhard Rod.

This application for Department of Transport Approval is submitted under the Individually Constructed Vehicle Category (LH5, LH6).

Design Philosophy

The design philosophy is to provide a specialist vehicle with similar appeal to a motor cycle, but with much greater safety than a two-wheeled vehicle. Thus, the vehicle is simple and spartan, without the offer of luxury refinements, such as weather protection, sun visors, or a heater. As an individually constructed vehicle, the owner and builder is able to tailor the construction to their own requirements.

Standard Dimensions

Wheelbase			2260mm

Front Track			1330mm

Rear Track			1330mm

Ground Clearance		   100mm (min)

Height to top of rollbar	1130mm (variable)

Overall width			1545mm

Weight			  600kg

Engines			up to 147 kW

Configuration

Three-dimensional space frame with structural sheet steel and aluminium bracing panels.

Panel				Thickness(mm)		Fixing Spacing (mm)

Floor				1.6				welded

Tunnel side, top		0.9				welded

Rear outside 			1.2				welded

Footwell			1.2				welded

Scuttle top			1.2				welded

Seat back			0.9				75mm

Exterior			1.2				50mm

All aluminium panels except transmission tunnel lid are riveted with steel pop rivets and bonded with Sikaflex  or equivalent construction adhesive sealant.

3.	STATEMENT OF AUSTRALIAN DESIGN RULE (A.D.R.) COMPLIANCE

This vehicle has been designed to comply with the Australian Design Rules, enabling the car to be registered under the Kit and Custom Vehicles provisions of the Vehicles Standards Regulations of the Road Traffic Act.

ADR 1 	REVERSING LAMPS.

ADR 2 	SIDE DOOR LATCHES & HINGES.

ADR 3 	SEAT ANCHORAGES.

ADR 4 	SEAT BELTS.

ADR 5 	SEAT BELT ANCHORAGES.

ADR 6 	DIRECTION INDICATOR LAMPS.

ADR 7 	HYDRAULIC BRAKE HOSES.

ADR 8 	SAFETY GLAZING MATERIAL

ADR 10 	STEERING COLUMN

ADR 11 	INTERNAL SUN VISORS.

ADR 12 	GLARE REDUCTION IN FIELD OF VIEW

ADR13   	INSTALLATION OF LIGHTING & LIGHT-SIGNALLING DEVICES.

ADR 14 	REAR VISION MIRRORS.

ADR 15 	DEMISTING OF WINDSCREEN.

ADR 16 	WINDSCREEN WIPERS & WASHERS.

ADR 18 	INSTRUMENTATION.

ADR 20 	SAFETY RIMS.

ADR 21 	INSTRUMENT PANEL.

ADR 22 	HEAD RESTRAINTS.

ADR 23 	PASSENGER CAR TYRES.

ADR 24 	TYRE & RIM SELECTION.

ADR 25 	ANTI-THEFT LOCK.

ADR 28 	EXTERNAL NOISE.

ADR 29 	SIDE DOOR STRENGTH.

ADR 31 	BRAKING SYSTEM.

ADR.37 	EMISSION CONTROLS.

ADR 42 	GENERAL SAFETY REQUIREMENTS.

ADR 43 	VEHICLE CONFIGURATION & MARKING

ADR 46 	HEADLAMPS.

ADR 47 	REFLEX REFLECTORS.

ADR 48 	REAR REGISTRATION PLATE ILLUMINATION.

ADR 49 	SIDE LAMPS & STOP LAMPS.

ADR 60 	CENTRE HIGH-MOUNTED BRAKE LIGHT.

ADR 1 REVERSING LAMPS.

q	One or two white lamps must be fitted at the rear,

q	at least 250 mm from the ground but not more than 1200mm.

q	If only one lamp is fitted it must be on the driver's side.

q	The lamp(s) must illuminate when reverse gear is selected and with ignition switch on or engine running.

q	Lamp(s) must be visible from 45 degrees outwards to each side,

q	15 degrees upward

q	5 degrees downward.

ADR 2 SIDE DOOR LATCHES & HINGES.

-Not applicable to Locost Sportscar.

ADR 3 SEAT ANCHORAGES.

Mountings

q	Each seat must be mounted to the floor using at least four 8mm Grade 8.8 (min) bolts,

q	backing, plates made from 3mm steel:

q	 40mm square (5mm radiused corners), or

q	50mm diameter.

Seat Structure

q	 Seats certified as ADR compliant, brand (eg Whitepointer)………..or

q	Bench seat integral with chassis (not requiring testing under ADR)

ADR 4 SEAT BELTS.

q	New seat belts complying with Australian Standard 2596 or an approved equivalent standard fitted to driver's and passenger's seats

q	Part Number Autoliv Klippan K1639, or

q	Other

ADR 5 SEAT BELT ANCHORAGES.

q	All seat belt mountings fitted with 7/16"–20AUNF threads to suit the bolts supplied with new seat belts.

q	Mountings fitted into plates made from 3mm mild steel 75mm x 50mm minimum (5mm radiused corners), welded too at least two 25mm RHS chassis members (page 8, S.A. DoT, No18a),

q	Upper anchorage mountings fitted into roll bar tubing, fitted into fully threaded crush tube. Crush tube welded, or supplied as a captive nut (page 8, S.A. DoT, No18a).

Mountings are corrosion protected:

q	Paint

q	Galvanising

q	Aluminium

q	Other (specify) ………….

ADR 6 DIRECTION INDICATOR LAMPS.

Front and rear indicator lamps

q	visible from 80 degrees outward

q	45 degrees inward,

q	15 degrees up and down,

q	mounted at least 350mm above the ground,

q	illuminating surface at least 40mm from the illuminating surface of the headlights.

q	at least 600mm apart

q	no more than 400mm from the outer edge of the car.

q	Part numbers (FRONT)………..

q	Marked as ADR compliant, or,

q	E-marked

q	Part numbers (REAR)………..

q	Marked as ADR compliant, or,

q	E-marked

Side indicators

q	Side indicators omitted as front indicators mounted on top of flared guards,  and achieve performance criteria listed below, OR,

q	visible from the rear, between 5 and 60 degrees outward.

q	at least 500mm above the ground

q	not more than 1800mm from the car front.

Indicator lamp operation

q	all lamps on the same side flash in phase between 60 and 120 times per minute,

q	visible dashboard lamp

q	audible alarm fitted.

ADR 7 HYDRAULIC BRAKE HOSES.

New brake hoses fitted are permanently marked with manufacturers name.

Brake hoses marked as complying with ADR 7 (or equivalent standard, eg FMVSS 1022)  fitted, OR

Manuafcturer has provided certification that brake hoses comply with ADR 7(or equivalent standard, eg FMVSS 1022),

ADR 8 SAFETY GLAZING MATERIAL

q	Vehicle fitted with aeroscreens, ADR not applicable,OR,

q	The windscreen glass  is indelibly marked with the relevant Australian Standard number and installed so that this marking remains visible.

q	Manufacturer:…………………………

ADR 10 		STEERING COLUMN

q	A collapsible steering column from a recognised manufacturer fitted,

q	Source vehicle incorporates the requirements of this ADR:

Make: ……………………

Model: ……………………

Year: ………………………

q	Original method of mounting retained

q	Manufacturer's shear clamps must be used to permit the column assembly to break away from its upper mounting in a severe impact.

Steering Wheel:

q	Original as fitted to column,

q	"aftermarket" wheel certified as complying with ADR 10.

ADR 11 			INTERNAL SUN VISORS.

This ADR does not apply as sun visors are not fitted.

ADR 12 			GLARE REDUCTION IN FIELD OF VIEW

No chromed or polished surfaces capable of reflecting fight into the driver's eyes are present in the drivers field of view, check following are painted, plastic coated or have matt or satin finish:

q	Windscreen frames,

q	windscreen wiper arms and wiper blade asembly

q	headlight shells,

q	instrument bezels,

q	rear vision mirror bracketry,

q	steering wheel and horn ring,

q	control levers and gearstick

q	windscreen pillars where visible to the driver.

q	Aluminium bonnet and scuttle will need to be painted

ADR 13 	INSTALLATION OF LIGHTING & LIGHT-SIGNALLING DEVICES.

q	Hazard warning lamps system fitted

q	All direction indicator lamps capable of flashing simultaneously, operated by a separate control which must function even with the engine switched off or with the ignition key removed.

q	A visible dashboard warning lamp e fitted

ADR 14 			REAR VISION MIRRORS.

Two mirrors are mandatory, both must be capable of adjustment from the driver's seat and both must have a flat reflecting surfaces. If a passenger's side mirror is fitted it may have a flat or convex reflecting surface and does not need to be adjustable from the driver's seat. The minimum field of view specified in this ADR presents no problem in a Locost Sportscar  .

ADR 15 			DEMISTING OF WINDSCREEN.

This requirement does not apply to Locost Sportscar  , unless hood fitted.

ADR 16 			WINDSCREEN WIPERS & WASHERS.

Not applicable as vehicle is fitted with aeroscreens, OR,

Windscreen wipers;

q	Two wiper arms, at least 130mm long fitted,

q	Two wiper blades,  at least 330mm long fitted,

q	Operate with two speeds, the higher at least 45 cycles per minute and the lower at least 20.

q	Area swept by wipers clears primary vision area, satisfying intent of ADR,

q	Screenwasher with a capacity of at least one litre fitted

q	Scerreen washer cleans area directly in front of driver and directly in front of passenger seat,.

ADR 18 			INSTRUMENTATION.

q	A "kilometres per hour" speedometer fitted. with an accuracy,, of +10%,-0% for all speeds above 40km/h.

q	An odometer accurate to +/-4% is fitted,

Discretion is sought as the ADR requires the odometer to handle a range of 999,999 kilometres, the most commonly used instrument goes only to 99,999. The Electronic VDO brand speedometers have 6 digits as std.

q	Engineers discretion granted

Field of View –

q	speedometer

q	other instruments

q	warning lights, whether mandatory or discretionary,

fall within the driver's field of view which is defined as 25 degrees to the right, 40 degrees to the left and not more than 35 degrees below horizontal.

q	Variable intensity illumination is necessary for the instruments.

q	 adjustable rheostat or

q	a high/low switch through a fixed resistor.

ADR 20 			SAFETY RIMS.

q	Wheel rims certified by manufacturer as complying with ADR 20 (certification attached), or

q	Marked as complying with ADRs or

q	Marked as “JJ “type.

Wheels aree indelibly marked with:

q	nominal diameter ……….inches

q	width …………. mm/inches

q	offset ………….mm/inches

q	manufacturer's name ………………………………….

q	Australian or equivalent Standard to which they were manufactured A.S.……………………………………...

ADR 21 		INSTRUMENT PANEL.

To reduce potential injury to occupants any likely "head impact areas" must be covered with high density energy absorbing crash padding material. In a Locost Sportscar this means at least the rear-facing scuttle lip surrounding the dashboard.

ADR 22 		HEAD RESTRAINTS.

q	Seat manuafcturere (………………………) certifies that seats com-ply with ADR 22 (a copy of certification is attached), OR,

q	Head restraints provided on both seats,

q	mounted on or integral with the seat backs.

q	Their width is at least 170mm

q	height, if separate, at least 115mm.

q	the lowest position of separate, adjustable type at least 750mm above the seat cushion.

ADR 23 		PASSENGER CAR TYRES.

Brand of tyres fitted is ………………………………..

q	Tyres are marked as complying with ADRs or DOT standards for construction,.

ADR 24 		TYRE & RIM SELECTION.

Size of Tyres fitted ……….x………. are appropriate for diameter of rims ……..inches

Speed Rating:

q	H-rated

q	V-rated

q	Z-rated

A durable "tyre placard" showing, tyre and rim size, recommended pressures in kPa, and a load rating/speed category statement is fitted under passenger side interior.

ADR 25 		ANTI-THEFT LOCK.

q	The steering lock mechanism in the steering coilumn is retained from ADR complying vehicle (make …., model…… year 19…..).

An approved vehicle immobilisation device has been fitted by:

q	The manufacturer …………OR,

q	An approved installer (name …………………… approval ref no…………..).

ADR 28 		EXTERNAL NOISE.

q	Vehicle is fitted with exhaust system that is free from defects, and all gases  are emitted to the atmosphere from the designed exit point

q	Exhaust exits to the rear of the vehicle (no side exit pipes)

q	Noise levels tested in accordance with the Code of Practice for Motor Vehicle Noise (June 1997) adopting the ATAC and ANZECC endorsed test procedure and limits and the Intergovernmental Agreement on the Environment.

q	Vehicle did not exceed a maximum noise level of 90 dB(A) at 4000 rpm (4 cylinder spark ignition engine).

q	Copy of report on test procedure attached

ADR 29 		SIDE DOOR STRENGTH.

Not applicable to Locost Sportscar  as no doors fitted

ADR 31 		BRAKING SYSTEM.

q	dual-circuit hydraulic system fitted

q	brake failure indicator lamp which can be operated either by:

q	 loss of pressure in one circuit, or

q	by loss of brake fluid,

q	Brake failure circuit includes a "bulb test" function, that switches on with ‘ignition switch’ in ‘on’ position.

q	The parking brake mechanically operated

q	The parking brake fitted with warning lamp.

ADR.37 		EMISSION CONTROLS.

q	The engine fitted is sourced from a vehicle which complies with ADR 37:

Engine designation (eg 4A-GE)…………………

(Vehicle make) ……. (model) ……(year)…..,

OR,

q	The engine fitted is equivalent to an engine used in a vehicle which complies with ADR 37:

Engine designation (eg 4A-GE)…………………

(make) ………. (model) …….…(year)…..,

OR,

q	The engine fitted is used in a vehicle which complies with an equivalent international standard (such as USA stanadrards) specified in ADR 37:

Engine designation (eg 4A-GE)…………………

(make) ……….…. (model) ……..……(year)…..,  OR

q	Vehicle is fitted with an LPG-only engine, and ADR 37 does not apply

q	LPG Installer is approved by Department of Transport

q	Name of LPG Installer ………………..,

q	Approval Number ……………….

q	Date of installation …………… (now go to ADR 42)

q	The engine is designed to run on unleaded petrol

q	The engine remains standard as manufactured and incorporate all the components and features originally fitted to that engine including all pollution-reducing devices aimed at evaporative fuel losses and exhaust emissions

q	A  "charcoal canister" is fitted in accordance with OEM to control vapourised fuel losses to the atmosphere

q	a catalytic converter.appropriate to the engine capacity is fitted

q	Within 150mm of the petrol tank filler a label is attached stating "UNLEADED PETROL ONLY" in letters 6mm high.

q	The petrol filler inlet is fitted with a post-1986 restrictor in the filler neck to prevent insertion of a leaded petrol nozzle,

Source vehicle for inlet restriction make ……… model ……. Year ……..

ADR 42 		GENERAL SAFETY REQUIREMENTS.

Bonnet latching—

q	secondary latchs fitted to forward-opening engine covers or hinged bonnets

Cigarette lighters,

q	only operate with ignition switch in "accessory" or "on" positions.

q

Electrical wiring-

q	Insulated, including no exposed metal connectors,

q	Wiring adequately supported at least every 600mm with cable ties or plastic ‘p’-clips

q	protected from chafing by grommets where it passes through panels,

q	wiring is positioned so it cannot contact moving parts, overheat or constitute a fire hazard due to proximity to the fuel system.

Exhaust outlet ---

q	to the rear, or to the right. The latter is an option with the recommended engine.

q	the pipe discharges at not more than 10 degrees above or 45 degrees below the horizontal.

q	Mudguards Locost Sportscar flared front guards comply, so do the optional cycle-type guards.

Audible warning, device ---

q	a horn or horns emitting a signal of constant amplitude and frequency are fitted

q	powered by electricity or compressed air.

q	Designed for automtive use:

q	Source vehicle: (make)………………….. (model)…………….. (year)  ….

q	Aftermarket items (manufacturer) ………………. (part No.) .,………..

ADR 43 		VEHICLE CONFIGURATION & MARKING

Identification number (VIN) unique 17-digit number is issued by the Department of Transport

q	to be stamped in a visible location on the chassis member ‘S’ or ‘T’ in 7mm high characters.

q	Engine number is visible with the engine installed Registration plates --- self explanatory.

q	Ground clearance of 100mm.

ADR 46 		HEADLAMPS.

q	Two headlamps fitted to Locost Sportscar  s,

q	Certified as ADR complying (see attached documentation)

q	Manufacturer: …………………… Part Number …………………..

q	installed in accordance with manufacturers instructions (including dimensions)

q	illuminating surfaces are positioned so that their inner edges are at least 600mm apart,

q	outer edges are not more than 400mm from the car's widest point,

q	lower edges not less than 500mm above the ground.

q	both lights are simultaneously switched on or changed from dip to high beam and vice-versa.

q	A blue main beam warning indicator fitted.

q	Dipped beam shall have a right-hand cut-off to prevent dazzle to oncoming drivers.

ADR 47 		REFLEX REFLECTORS.

q	Certified as ADR complying (see attached documentation)

Manufacturer: …………………… Part Number …………………..

q	installed in accordance with manufacturers instructions (including dimensions)

The size, shape. location and orientation of reflex reflectors mandatory on the rear of all cars.Suitable reflectors are incorporated into the recommended rear light clusters, and their mounting on the body ensures the requirements are met.

ADR 48 		REAR REGISTRATION PLATE ILLUMINATION.

q	Certified as ADR complying (see attached documentation)

Manufacturer: …………………… Part Number …………………..

q	installed in accordance with manufacturers instructions (including dimensions)

registration plate:

q	positioned on the spare wheel carrier, or

q	mounted on the body,

ADR 49 		SIDE LAMPS & STOP LAMPS.

q	Certified as ADR complying (see attached documentation)

Manufacturer: …………………… Part Number …………………..

q	installed in accordance with manufacturers instructions (including dimensions)

q	Two white position lamps are fitted at the front.

q	at least 350mm above the ground,

q	600mm apart

q	not more than 400mm from the widest point and

q	visible from 45 degrees inward,

q	80 degrees outward.

q	15 degrees above and below the horizontal.

q	incorporated in the headlights.

Two red position lamps are fitted at the rear.

q	at least 350mm above the ground,

q	600mm apart

q	not more than 400mm from the widest point and

q	visible from 45 degrees inward,

q	80 degrees outward.

q	15 degrees above and below the horizontal.

.

Two red stop lamps are fitted at rear

q	at least 350mm above the ground,

q	600mm apart

q	not more than 400mm from the widest point and

q	visible from 45 degrees inward,

q	45 degrees outward.

q	15 degrees above and below the horizontal.

q	Stop lamps illuminate when the brake is applied but (need not operate with ignition switched off).

ADR 60 		CENTRE HIGH-MOUNTED BRAKE LIGHT.

q	Certified as ADR complying (see attached documentation)

Manufacturer: …………………… Part Number …………………..

installed in accordance with manufacturers instructions (including dimensions)

q	Brake light located on the car's median longitudinal plane, ie the

q	centreline,

q	Centre high mounted brake light illuminates in unison with the pair of  stop lights when brakes are applied.

4.		CERTIFICATE OF CONFORMITY

The subject vehicle a Locost Sportscar assembled by:

…………………………………of ……………………………………………………….

Has been inspected by a representative of the Locost car Club of W.A. at the following stages of assembly

| Stage of Assembly | Date of Inspection |
| --- | --- |
| Running gear, suspension, engine and Chassis complete without body attached |  |
| Complete and untrimmed |  |
| Complete |  |

The inspections revealed that the assembly has been carried out in accordance with Engineering Submission No. 01- 0305 prepared by the Locost Car Club of Western Australia. The quality of workmanship and materials employed was of an acceptable standard.

The vehicle has been tested for external noise level and the following noise levels were recorded.

Static Test : engine RPM ………………….

Noise Level (left 45o)			Noise Level (left 45o)

……… dB(A) …………dB(A)		……… dB(A) …………dB(A)

Chassis Number: …………………….

Engine Make and Capacity: ……………….

Engine Number: …………………………

Year of Engine Manufacture: ………………………

Signed: ……………………………….	Locost Car Club of Western Australia

APPENDICES:

APPENDIX A	LOCOST DIAGRAMS

APPENDIX B	ENGINEERING CHASSIS UPGRADE DRAWINGS

APPENDIX C	ADR COMPLIANCE CERTIFICATION & DOCUMENTATION FROM COMPONENT MANUFACTURERS

APPENDIX A

LOCOST DIAGRAMS

Every diagram from Ron Champion books

(if book is acknowledged in full no problems with copyright)

APPENDIX B

ENGINEERING CHASSIS UPGRADE DRAWINGS

Jamie Guards drawings go here

APPENDIX C

ADR COMPLIANCE CERTIFICATION & DOCUMENTATION

FROM COMPONENT MANUFACTURERS

Photocopies of instruction sheets etc that come with lights and other parts, confirming ADR compliance